## Slide 1
Smart Bird Feeder
Stevie Nicks and the Xaybanha Zhous – Group 9 – 12/9/2020 – Version 1.0
Calvin Xaybanha, Stephanie “Stevie” Taylor, Zeming Zhou, Nickolas Short

## Slide 2: Problem Statement
The problem is that crows and squirrels eat the seed meant for small birds, and that this decreases the ability of bird feeder owners to increase the species richness of birds in their area.
If squirrels and crows learned the device will not feed them, they will keep away from the smart bird feeder and that will satisfy bird watchers.
Concerned ecologists would also rest easier if more species were able to compete.
Notes: per the 2016 National Survey of Fishing, Hunting, and Wildlife-Associated Recreation

## Slide 3: Motivation
An easy way for bird watchers to feed small birds.
It is important because the species richness of urban ecology is what keeps us healthier.
Ostfeld & Keesing. 2000. Biodiversity and disease risk: the case of Lyme disease. Con. Bio. 14:722-728.

## Slide 4: Concept of Operation
The automatic bird feeder was designed to dispense
bird feed to birds when a small bird is “detected”.
The automatic bird feeder detects the small bird if it
mounts onto the perch where the force sensor is affixed if it weighs less
than 500g and if the bird’s chirping is audible to the microphone and
above 50Hz.
After a bird is detected, the servo motor will rotate +45 degrees to
open a gate to the bird feed reservoir, and bird feed will fall into a
basin. Less than one second has passed since opening, the motor will
close the gate with a -45 degree rotation to stop the flow of bird feed
and return to its original position.

## Slide 5: Alternatives
Bird feeders already available on the market can feed small birds. The success or even attempt to repel squirrels and crows depends on the bird feeder, but in all cases they don’t also teach the bird to chirp for its food.

## Slide 6: Requirements
Must automatically dispense bird feed when a bird is "detected“
Must be able to "feed" only small birds
Must use a microcontroller to control servo based on microphone and weight sensor

## Slide 7: Design – Hardware – Level 0
We had to redesign to use a weight/force sensor to determine small bird vs crow/squirrel instead of only frequency. There isn’t sufficient difference between frequency of squirrels to birds to only use audio.

## Slide 8: Design – Hardware – Level 1

## Slide 9: Design – State Transition Diagram
IDLE
ADC
WAIT
DOOR
NO_SOUND
SOUND
READING
WRONG_MASS
SOUND
RIGHT_MASS
DOOR_MOVING
DOOR_CLOSED
DOOR_CLOSED
FEED_AGAIN

## Slide 10: Design – Software (Overview)
Utilized Arduino IDE for its good selection of built-in functions (analogRead, digitalWrite, etc.) as well as prepackaged libraries—namely the Servo library.
Fairly simple program with few lines of code when using the IDE.

## Slide 11: Design – Software (Code)
// Some useful #defines
#define WT_MIN 100
#define WT_MAX 450
#define MIC_PIN 2
#define WEIGHT_PIN A5
#define SERVO_PIN 3
#define TRAVEL_ANGLE 90
#define ANGLE TRAVEL_ANGLE / 2
#define OPEN_TIME 1500
#define WAIT_TIME 30000
// Variables
Servo gateServo;
int weightMeasurement = 0;
void setup() {
gateServo.attach(SERVO_PIN);
pinMode(WEIGHT_PIN, INPUT);
pinMode(MIC_PIN, INPUT);
}
void loop() {
if(digitalRead(MIC_PIN)) {
weightMeasurement = analogRead(WEIGHT_PIN);
if( (WT_MIN <= weightMeasurement) &&
(weightMeasurement <= WT_MAX) ) {
cycleChuteDoor();
}
else delay(250);
}
}
void cycleChuteDoor() {
myservo.write(90-ANGLE);
delay(OPEN_TIME / 2);
myservo.write(90+ANGLE);
delay(OPEN_TIME / 2 + WAIT_TIME);
}

## Slide 12: Design - CAD

## Slide 13: Implementation - Schematic

## Slide 14: Implementation - Tools
Hardware:
Oscilloscope
Digital Multimeter
Power Supply
Software:
EagleCAD
Fusion360
Arduino IDE
LTSpice
Microsoft Project

## Slide 15: Implementation - BOM
Notes: Total cost per person for this project was $43.58 x 4 = $174.32

## Slide 16: Prior Work
The competition for smart bird feeders are focused on bird watchers with smart cameras – none focus on smart selectivity in using weight to not feed squirrels and crows.
These are currently in development, there is no existing smart bird feeder that a user can buy off the market.

## Slide 17: Contributions
Calvin – Schematic, board design, prototyping the ATTiny to control the servo motor
Stevie – Organizing, ordering parts, prototyping, writing
Zeming – Ordering parts, prototyping, writing
Nick – Prototyping, coding, testing, board layout
Notes: Calvin - I contributed to the schematic and board design. I did some tests using the ATTiny to control the servo motor, such as finding the PWM signal whose duty cycle is controlled by a 10K ohm potentiometer to get a clockwise rotation, counterclockwise rotation, and no rotation.

## Slide 18: Lessons Learned
Calvin – Always view the datasheet of a part before purchasing it and use parts more suitable for prototyping.
Stevie – Do better research on parts before purchasing and check rubrics (i.e. client emails, paperwork explaining the requirements) before turning in homework (paperwork the client asked for).
Zeming - How to communicate effectively with teammates, look for electrical components, and design some simple PCBs.
Nick –Implement the 1-wire Debug functionality in the device to allow for outputting register values.
Notes: Calvin - I learned that you should always view the datasheet of a part before purchasing it, unless it is not provided. I would definitely change some parts to be more suited to prototyping. For example, the continuous rotation servo motor changed to a normal servo, and ATTiny13 to a different controller IC with more I/O pins, and more allocated memory for uploading programs.

## Slide 19: Lessons Learned – Design Review
Schematic:
  Need to add linear regulator and make sure voltage nets are applied properly.
  Add ISP header.
Board:
  Need thicker traces all around.
  Primarily surface mount components.
  Need to add stitching vias.
Notes: Calvin - I learned that you should always view the datasheet of a part before purchasing it, unless it is not provided. I would definitely change some parts to be more suited to prototyping. For example, the continuous rotation servo motor changed to a normal servo, and ATTiny13 to a different controller IC with more I/O pins, and more allocated memory for uploading programs.

## Slide 20: Questions? …On to the demo!
Notes: Calvin - I learned that you should always view the datasheet of a part before purchasing it, unless it is not provided. I would definitely change some parts to be more suited to prototyping. For example, the continuous rotation servo motor changed to a normal servo, and ATTiny13 to a different controller IC with more I/O pins, and more allocated memory for uploading programs.